## Slide 1
G.Trubnikov, I.Meshkov
on behalf of the team
RT-6 Italy-JINR, Dubna, 04/03/14
NICA collider complex at JINR:
challenges and perspectives
1

## Slide 2
Au x Au collisions
The First Proposals:
Towards Searching for A Mixed Phase of Strongly Inteacting QCD Matter
at The JINR Nuclotron
A.N. Sissakian, A.S. Sorin, M.K. Suleymanov, V.D. Toneev, and G.M. Zinovjev
arXiv:nucl-ex/0601034 v1 24 Jan 2006
A.N. Sissakian, A. S. Sorin, and V. D. Toneev
Proc. of the 33rd Intern. High Energy Physics conference, ICHEP’06,
Moscow, Russia 1, 421 (2006), nuclth/0608032
An optimal way to reach
the highest possible baryon density is
heavy ion collision at SNN = 4 - 11 GeV/u

## Slide 3
Colliders and fixed target experiments
Fixed target experiment: a particle beam extracted from an accelerator bombards an immovable (“fixed”) target
Colliding beams
Both primary particles and generated in collision with fixed target move with the speed of the center of the mass in direction of primary (bombarding) particle!
NICA Project at JINR Igor Meshkov 16th Lomonosov Conference LMSU 23 August, 2013

## Slide 4: Collider vs Fixed target
Center of mass energy (S)
 | Collider | Fixed target
Accurate formulae |  | 
Similar particles (symmetric) |  | 
Ultra-relativistic case |  | 
SIS300: B = 300 Тm, EAu = 36 GeV/u Еcm ~ 8 GeV/u
Nuclotron: B = 45 Тm, EAu = 5.5 GeV/u Еcm ~ 3.3 GeV/u
NICA: B = 45 Тm, EAu = 5.5 GeV/u Еcm ~ 11 GeV/u
RHIC: B ~ 130 Тm, EAu = 100 GeV/u Еcm ~ 14 GeV/u

## Slide 5
Colliders and fixed target experiments
1956, D.W.Kerst et al., – First proposal, pp collider
History of colliding beams
1958 - 1965 VEP, INP at Novosibirsk
G.Budker, A.Naumov, A.Skrinsky, S.Popov, V.Sidorov, G.Tumaikin et al.
e-e-, 2 x 160 MeV,
L = 31027 cm-2s-1
1958 - 1965 SLAC
Princeton-Stanford group:
G. K. O'Neill, B.Richter et al.
e-e- collider 2 x 500 MeV
G.K.O'Neill
Wolfgang ("Pief") Panofsky

## Slide 6: Parameters and luminosity calibration: ISR
beam energy (p): 31 GeV
proton-proton collider and proton-antiproton collider
two separate beam pipes – different orbits for the two beams
coasting beams (no bunches)
collision at large angle in horizontal plane
beam current of up to 40A
very large beams (size in the order of cm)
beam separation with magnets
calibration done for proton-proton and proton-antiproton collisions

## Slide 10
CBM @ FAIR/SIS-100/300
Fixed target, E/A=10-40 GeV, high luminosity
STAR/PHENIX @ BNL/RHIC.
designed for high energy researches (√sNN > 20 GeV),
low luminosity for LES program L<1026 cm-2s-1 for Au79+
NA61 @ CERN/SPS.
Fixed target, non-uniform acceptance, few energies
(10,20,30,40,80,160A GeV), poor nomenclature of
beam species
MPD & SPD @ JINR/NICA.
Collider, small enough energy steps in the range
√sNN = 4-11 GeV, a variety of colliding systems,
L~1027 cm-2s-1 for Au79+
2nd generation HI experiments
3nd generation HI experiments
Notes: 10

## Slide 11
Colliders and fixed target experiments
Collider
fixed target
Baryon density in Au + Au collisions
at SNN = 4 - 11 GeV/u
J.Randrup,
J.Cleymans
PR C74 (2006)
047901
RHIC
SPS
E1+E2: collider
E: Fixed Target
Nuclotron / BMN
SIS-100
NICA/MPD
SIS-300 (FAIR)

## Slide 12
Unique Dubna technologies of fast-cycling superconducting magnets tested during several tens of Nuclotron runs and chosen as basic for accelerator complexes NICA and FAIR
Common European Research infrastructure for Heavy Ion High Energy Physics: NICA + FAIR
Notes: 12

## Slide 13
1a) Heavy ion colliding beams 197Au79+ x 197Au79+ at
sNN = 4 ÷ 11 GeV (1 ÷ 4.5 GeV/u ion kinetic energy )
at Laverage= 1x1027 cm-2s-1 (at sNN = 9 GeV)
1b) Light-Heavy ion colliding beams of the same energy range and L
2) Polarized beams of protons and deuterons in collider mode:
pp spp = 12 ÷ 27 GeV (5 ÷ 12.6 GeV kinetic energy )
dd sNN = 4 ÷ 13.8 GeV (2 ÷ 5.9 GeV/u ion kinetic energy )
Laverage  1x1030 cm-2s-1 (at spp = 27 GeV)
3) The beams of light ions and polarized protons and deuterons for fixed target experiments:
Li  Au = 1  4.5 GeV /u ion kinetic energy
p, p = 5 ÷ 12.6 GeV kinetic energy
d, d = 2 ÷ 5.9 GeV/u ion kinetic energy
4) Applied research on ion beams at kinetic energy
from 0.5 GeV/u up to 12.6 GeV (p) and 4.5 GeV /u (Au)
NICA goals

## Slide 14
2nd IP
Notes: 14

## Slide 15
NICA: Nuclotron based Ion Collider fAcility
Routine
beam extraction at 5.2 GeV/u
Acceleration up to 5.8 GeV/u (C6+)

## Slide 16: Veksler & Baldin Laboratory of High Energy Physics, JINR
extracted beam area
Nuclotron
Lu 20
accelerator facility
Booster
New Linac
Collider
X
X
SPD
MPD

## Slide 17: Progress in ion sources development and commissioning Heavy ion source: Krion-6T ESIS Source for polarized particles (SPP)
B= 5.4 Tesla magnetic field reached in a robust regime. Full-scale tests of new ESIS in reflex mode of operation was started in spring 2013.
Source is assembled in 2013
and works on its commissioning had been started in June 2013. The goal is to get 1010 deuterons per pulse.
17
Test gold ion beams have been produced:
- Au30+ ÷ Au3232+, 6108, Tioniz= 20 ms for
Au32+ -> repetition rate 50 Hz.
- ion beams Au51+ ÷ Au54+ are produced.
Now the goal is: production of Au65+ ÷ Au69+
ion beams for their possible injection into
LU-20 -> Nuclotron in spring 2014.

## Slide 19
Injection
from HILac
Extraction
to Nuclotron
Satellite refrigerator,
Measurement period,
Energy evacuation
Electron cooling
RF
HILac
LU20
19
Booster synchrotron

## Slide 20
2.3 m
4.0 m
Prototype of the Booster dipole
The best method to measure phase space size
В.И.Векслер
Tunnel preparation
NICA Booster synchrotron

## Slide 21
Unique low energy (1-4.5 GeV/u) collider with extremely high luminosity L=1e27
FODO structrure
To reach maximum peak luminosity:
minimum beta function in the IP;
maximum bunch number;
maximum bunch intensity;
minimum beam emittance;
minimum bunch length.
Fruitful collaboration between JINR, FNAL, BNL, FZJ, CERN:
- beam dynamics, tracking;
- electron clouds effect;
- beam stacking and cooling;
- lattice expertise;
Chart: Luminosity @ NICA as function of particle number (to avoid incoherent tune shift) and energy
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5
L@dQ<=0,05 | 1e+25 | 5.34e+25 | 1.79e+26 | 4.7e+26 | 1.016e+27 | 1.99e+27 | 3.6e+27 | 5.98e+27

## Slide 22
Collider 4T
(CRing = 251.5 м)
September 2009
Collider
2T - 350
(CRing = 350 m)
February 2010
Collider
2T- 534
(CRing = 534 m)
July 2010
Three first versions
The Versions of The NICA Collider Project

## Slide 23
2nd IP
Notes: 23

## Slide 24
Collider parameters
Ring circumference, m | 503,04 |  | 
Number of bunches | 23 |  | 
Rms bunch length, m | 0.6 |  | 
Beta-function in the IP, m | 0.35 |  | 
Ring acceptance (FF lenses) | 40  mm mrad |  | 
Long. acceptance, dp/p | ±0.010 |  | 
Gamma-transition, gtr | 7.091 |  | 
Ion energy, GeV/u | 1.0 | 3.0 | 4.5
Ion number per bunch | 2.75∙108 | 2.4∙109 | 2.2∙109
Rms momentum spread, 10-3 | 0.62 | 1.25 | 1.65
Rms beam emittance, h/v, (unnormalized), mmmrad | 1.1/ 1.01 | 1.1/ 0.89 | 1.1/ 0.76
Luminosity, cm2s1 | 1.1e25 | 1e27 | 1e27
IBS growth time,sec | 186 | 702 | 2540
Peak luminosity can be estimated as:
The collision repetition rate:
Hour-glass effect ~ 1 ( because in our case s << *):
Maximum luminosity is reached when the bunch phase volume corresponds to the ring acceptance
Chart: Luminosity @ NICA as function of particle number (to avoid incoherent tune shift) and energy
| 1.0 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5
L@dQ<=0,05 | 1e+25 | 5.34e+25 | 1.79e+26 | 4.7e+26 | 1.016e+27 | 1.99e+27 | 3.6e+27 | 5.98e+27

## Slide 25
Colliders and fixed target experiments
Luminosity
Luminosity is a parameter of an experiment with particle beams equal to event number per time unit (rate) if the process under study has cross section of  =1.
Luminosity is measured in cm-2s-1.
for fixed target experiment
for colliding beams
N1, N2 – particle number in colliding beams, S – maximal cross-section of two beams, f – frequency of collisions (for collider - particle rvolution frequency in the ring);
n0 – target density (cm-3), l – target thickness, dN/dt – particle flux bombarding the target.

## Slide 26: Luminosity
Limitation by particle rate production
- Total cross-section of particle losses
Effective use of the beam: reaction ~ loss

## Slide 27: Maximal achievable luminosity, average
Lmax = 107/5·10-26 = 2·1032 cm-2 s-1
Examples:
NICA: Ion generation rate: 109 per 4 seconds, reaction cross-section = 7 barn
PANDA (FAIR)
Antiproton production rate 107 / sec, cross-section 0.05 barn
CBM (FAIR)
Acceleration at SIS300 up to 1010 U ions, extraction during 10 sec
Lmax ~ 1032 cm-2 s-1
RHIC (100 GeV/u), cross-section ~ 219 barn
Lmax ~ 51029 cm-2 s-1

## Slide 28: Cycle parameters limitations
Lmax ~ 1.21030 cм-2 с-1 *1/4 /4 ~ 81028 cm-2 s-1
RHIC
Filling of both rings
And acceleration up to E_exp ~ 15 min
Experiment duration (L_lifetime) ~ 4 hours
Average luminosity RHIC 1028 cm-2 s-1 –
During experiment decreases by 20-30%
Due to stochastic ooling it is planned to increase luminosity by several times
This will require more intensive collider filling (more often)

## Slide 29
NICA
It is planned to fill both rings during 200 sec,
Experiment (luminosity) lifetime ~ 2000 sec
Lmax ~ 3.61031 cm-2 s-1 *2 /20 ~ 3.61030 cm-2 s-1
At designed luminosity 1027 cm-2 s-1 and stabilization of beam emittances due to beam cooling, the luminosity of experiment is practically constant
(if main loss mechanism is defined by interaction at Collision Point)
Limitation to the experiment characteristical time is connected to losses
due to interaction with residual gas
NICA Injection chain is designed with reserve of k~ 50

## Slide 30: Limitations caused by Detector possibilities (event count)
Each detector sub-system has technical limitations on event count and registration
Rate of MPD is 7 kHz
In the fixed target experiment we can control optimal detector load by varying width of the target.
But during energy scan the geometry of the reaction products changes

## Slide 31
Luminosity for fixed target experiment
Luminosity for internal target experiment
 - target width in atoms per cm2
First colliding beam is internal target for the second beam in the collider

## Slide 32
Collider luminosity
z
x
y
v1
x
y
z
v2
For colliding bunches

## Slide 33
For similar round-shape bunches colliding at zero angle:
to increase number of bunches -> parasitic collisions;
to increase bunch current -> coherent instability;
to decrease emittance (bunch size) –> incoherent tune shift -> resonanses;
to decrease IP beta-function -> severe demands to FF QL, chromaticity;
to increase rev. frequency -> to decrease circumference (no space for equipment)
to have optimal bunch length (“hour-glass” effect).

## Slide 34
Example of the optic structure in the IP region
lmin
Another limitation:
«electron clouds» effect: ion beam losses due to interaction with secondary electron avalanches from vacuum chambers walls
Max.beam size

## Slide 35
Bunch length
Hour-glass effect
* = 0.5 m

## Slide 36
Space charge effect limitations to Luminosity
Beam-beam effect and incoherent tune shift
Nb = const
Bunch-by-bunch
injection
Accumulation in
collider

## Slide 37
 | RHIC | NICA
Circumference, m | 3800 | 503
Bunch spacing, m | 3800/120 = 32 (electron clouds, injection, parasitic collisions) | 15 (distance between dipoles)
Beta-function at IP | 5 | 0.35
Distance from IP to FFL | 50 | 5
3.5 GeV/u
RHIC < 1025 cm-2s-1
NICA  1027 cm-2s-1

## Slide 38
IntraBeam scattering (IBS)
IBS leads to 3 independent effects:
-“Maxwellisation” of the distribution fuction;
Equal energy swaping between all 3 degrees of freedom
Increasing of the 6D phase volume
Why IBS differs from situation when molecules interact? -
Cyclic accelerators because of curvature sections (arcs, etc) have Dispersion.
Due to Dispersion the variation of the longitudinal coordinate leads to
The variation of transverse oscillation amplitude.
By other words transverse and longitudinal motion are coupled.
Single scattering on large angles – Touschek effect
There is no way to keep Luminosity without beam cooling !!!

## Slide 39
Luminosity life-time
Without beam cooling - beam emittance grows due to intra-beam scattering
Characteristic time of the luminosity decrease rate
~ several minutes (at RHIC operating with 100 GeV/u ~ 4 hours)
RHIC:
Construction of the Electron cooling system at low energy ions (< 5 GeV/u),
Stochastic cooling is used at maximal energy.
NICA:
Electron + stochastic cooling during beam stacking,
Electron + stochastic cooling during the experiment (collision mode)

## Slide 40
Electron Cooling
superposition of a cold intense electron beam with the same velocity
ve = vi
Ee=me/MiEi
e.g. :220 keV electrons cool 400 MeV/u ions
electron temperature
kBT  0.1 eV
kBT  0.1 - 1 meV
momentum transfer by Coulomb collisions
cooling force results from energy loss in the co-moving gas of free electrons
Courtesy to M.Steck

## Slide 41
Stochastic Cooling
First cooling method which was successfully used for beam preparation
Conditions:
Betatron phase advance (pick-up to kicker): (n + ½) 
Signal travel time = time of flight of particle (between pick-up and kicker)
Sampling of sub-ensemble of total beam
Principle of transverse cooling:
measurement of deviation from ideal orbit
is used for correction kick (feedback)
S. van der Meer, D. Möhl, L. Thorndahl et al.
pick-up
kicker
amplifier
Courtesy to M.Steck

## Slide 42
    Scrappers and collimators
The problems we have met and the solutions
The problems:
Beam space charge effects
Beam-beam effects
IntraBeam scattering (IBS)  luminosity degradation
The solutions:
Electron cooling application
Stochastic cooling application
Beam parameters choice
Operation scenario optimisation
Recombination in e-cooler
Bunch halo formation 
 parasitic collisions, background growth

## Slide 43
cool(Ei, Te, B)
recombn(Ei, Te)
Two regimes and cooling methods: injection & storage
Injection periodicity
Requirement:
cool  10 sec << recombination ~ 480 sec (for e-cooling)

## Slide 44
1. Facility structure and operation regimes
Electron cooling application! (N_ion)bunch  2E9!
Two collider regimes
Ni
Ion/bunch,
1E9
(IBS)x, y , sec
(cool)x , sec
recombination , sec
Tx = 2.5 eV
Bsol = 1 kG
, 1E-4
mmmrad
Ei – ion energy,
GeV/u
Luminosity
1E27 cm-2s-1

## Slide 45
Collider parameters
Parameter | Value
Circumference, m | 503.04
Max. magnetic rigidity, Tm | 45.0
Max. magnetic field, T | 1.8
Acceptance, mmmrad | 40.0
Longitudinal acceptance (p/p) |  0.01
Number of dipole magnets | 80
Collider
FODO, 12 cells x 90o each arc,
tr = 7.091 ,  * = 0.35 m (variable)

## Slide 46
Barrier Bucket method with electron cooling application!
1. Facility structure and operation regimes
Two regimes and cooling methods: injection & storage
Questions:
1. What kind of storage method?
2. What about storage with stochastic cooling application?
Problems below 2.5 GeV/u  studies in progress…
3. What kind of acceleration system is proposed?
Barrier Bucket system.

## Slide 47
Barrier RF system (1-st RF)
accumulation
barriers are switched off
coasting beam
2-nd RF system (h=C/21.5m)
1/3
bunching with adiabatic RF increase
Stop at length of 1/3 of bucket
3-d RF system (h=h2x3)
rebucketing adiabatic RF increase
bunch has final parameters
Proposed Scheme of Ion Stacking and Bunch Formation in The Collider
All stages are provided with cooling

## Slide 48
RF voltage of 2 kV at plateau duration up to 25 sec,
bunching factor (peak/mean current) ~ 5 (for NICA ~ 15)
Stochastic cooling of the carbon beam 2.5 GeV/u
Nearest plans: heavy ions, large bunching factor
s = 4.2 m
Spectrum analyzer
Computer reconstruction
Coasting beam
Bunched beam
48

## Slide 49: Collider Electron cooling
49
Maximum electron energy, MeV | 2.5
Cooling section length, m | 6.0
Electron beam current, A | 0.5-1
Electron beam radius, cm | 1
Magnetic field in cooling section, T | 0.1-0.3

## Slide 50
3. Start configuration of The NICA Accelerator Complex
No electron cooling system
Reduced (initial) version of stochastic cooling system
Reduced version of RF system consisting of
- Barrier bucket RF system
- RF-2 or RF-3 reduced systems (to be decided)
Operation in the ion energy range of 3.0  4.5 GeV/u
NICA MAC October 17-18, 2013
Disadvantage: beam intensity will be much lower of design value;
Advantage: at low beam intensity one can neglect with parasitic collisions in the straight sections!

## Slide 51
Startup version of the collider
Stacking with BB + Stoch. longitudinal cooling
Bunching at h = 22 and Stoch. longitudinal cooling
Bunch length is about 1.2 m (instead of 0.6 m)
Momentum spread of 4.210-4 (instead of 1 10-3)
Bunch intensity 5 108 (instead of 2 109)
Luminosity (17) 1025 cm2s1
Energy range from 3 to 4.5 GeV/u (optimum ~ 3.5 GeV/u)
Operation scenario:
Parameters

## Slide 52
  Activities
  AC Loss Reduction (exp. tests, FEM)
  2D/3D Magnetic Field Calculations (OPERA, ANSYS, etc.)
  Mechanical Analysis and Coil Restraint (design, ANSYS)
  (>Fatigue of the conductor and precise positioning)
Fast Ramped S.C. Magnets
R&D Goals
Reduction of eddy / persistent current effects
at 4K (3D field, AC loss)
Improvement of DC/AC-field quality
Experimental studies with modified Nuclotron magnets in JINR
Guarantee of long term mechanical stability (≥ 2108 cycles )
B_field error at R= 30 mm ≤ 210-4

## Slide 53
31/34
Test on vacuum tightness of the tubes for cooling the yoke
Collider magnets construction

## Slide 54
Full-scale Nuclotron–type superconducting model dipole and quadrupole magnets for the NICA booster and collider were manufactured at Laboratory of High Energy Physics JINR. First dipole and quadrupole magnets for the NICA booster have successfully passed the cryogenic test on the bench. 3 pre-serial dipole magnets for the NICA booster will be manufactured and tested this year. Serial production of the magnets for the booster is scheduled for 2014. Cryogenic tests of the model twin aperture dipole and quadrupole magnets for the NICA collider are scheduled for the first half of this year.
Sextupole corrector prototype (for SIS100 and NICA booster) at assembly
Booster dipole at cryo-test (9690A) and magnetic measurements
Twin aperture dipole magnet for Collider was tested June 2013 up to 11 kA

## Slide 55
Excellent co-operation:
JINR is responsible for delivery of 175 Quadrupole Units for SIS-100.
Collaboration Contract is prepared. It will include: manufactury, assembly cold testing of all QU’s. Investments from BMBF to JINR to the dedicated Test Facility which will be used for assembly and testing of SC magnets both for NICA and FAIR
First step: R&D Contract for equipment of the Test Facility signed between GSI and JINR in Dec’2013.
Intelligent equipment for cold measurements of the magnetic field in SC magnets is developed in Dubna and in Darmstadt. We exchange with technologies and experience (V.Borisov, P.Schnitzer, H.Khodzhibagiyan, E.Fischer, S.Kostromin, A.Donyagin)

## Slide 56
56
SC magnets assembly and test area (b.217):
cooperation with German centers
Workshops for SC coil production

## Slide 57
57
30 Dec 2013
On-line web-camera
http://betacool.jinr.ru/b/
On-line web-camera
http://betacool.jinr.ru/b/

## Slide 58
Already signed agreements in cooperation with:
CERN
GSI
State committee in science
& technology of Belarus
Kurchatov Federal Center
Institute for Nuclear Research RAS
Moscow State University
Budker Institute of Nuclear Physics RAN
Tsinghua University, China
Institute of Plasma Physics CAS, China
University of Science and
Technology of China
and others
58

## Slide 59
NICA accelerator complex - I
Nuclotron (45 Tm)
injection of one bunch
of 1.1×109 ions,
acceleration up to
1 - 4.5 GeV/u max.
Stripping (80%) 197Au31+ => 197Au79+
Linac HILac
KRION
Booster (25 Tm)
1(2-3) single(multi)-turn injection,
storage of 2 (4-6)×109,
acceleration up to 65 MeV/u,
electron cooling, acceleration
up to 600 MeV/u
Two SC
collider rings (Au x Au ions)

## Slide 60: …What NEXT ?...

## Slide 61
Motivation:
“Experiments with spin have killed more theories than any other single physical parameter.” (J.D.Bjorken)
[Cited by Elliot Leader, “Spin in Particle Physics”, Cambridge Univ. Press, 2001]

## Slide 62
NICA – II accelerator complex
Nuclotron (45 Tm)
acceleration up to
1 – 11 GeV max.
Linac LU-20
 p,d
sources
Two SC
collider rings (p x p)
spp = 25 GeV
Booster (25 Tm)
acceleration
up to 1 GeV/u

## Slide 63
NICA - III accelerator complex
Nuclotron 45 Tm
Stripping (80%) 197Au31+ => 197Au79+
Two SC
collider rings
Linac HILac
KRION
Booster 25 Tm
Two SC
Rings
~11 Tm
Merging bare
U235 beams
E~ 0,6GeV/u

## Slide 64
(point charge)
Zmax=1/α=137
where α is fine-structure constant
Heaviest atoms in QED
SHE
Hg
(finite size)
Zmax≈173
Yu. Oganessian 2013

## Slide 65
rmax - principal maximum
of the wave function
of the outermost orbital
Yu. Oganessian 2013
SHE-Factory
Zmax
Collider NICA

## Slide 66
U
U
Z=92+
Z=92+
ΔECM= 5-6 MeV·A
U
e-
U
e-
Z=91+
Z=91+
e+
e+
Yu. Oganessian 113-th Session of the Scientific Council of JINR, Feb.21, 2013, Dubna
SIMULATION OF
THE SUPERHEAVY ATOM
empty
K-shell
Z=184+
NICA
merging beams
U92+
U92+
U92+
U92+
U35+
BUSTER
NUCLOTRON
RINGS
ΔELAB= 2 GeV·A
NICA

## Slide 67
NICA - IV accelerator complex
Nuclotron (45 Tm)
acceleration up to
1 - 4.5 GeV/u max.
Stripping
Two SC
collider rings:
e- (1 GeV) x i (1 GeV/u)
Linac HILac
KRION
Booster (25 Tm)
acceleration
up to 600 MeV/u
SC e-Linac (30 MV/m)
e-
Nuclear physics:
e- beam is scan for heavy nuclei PDF
Target
Mass-separator
Radioactive ions

## Slide 68: Cos- Dipoles
Block number | 5
Turn number/quadrant | 34 (17+9+4+2+2)
Operating current | 8924 A
Yoke inner radius | 98 mm
Peak field on conductor (with self field) | 4.90 T
Bpeak / Bo | 1.09
Working point on load line | 69%
Current sharing temperature | 5.69 K
Inductance/length | 2.9 mH/m
Stored energy/length | 116.8 kJ/m
Discorap-Project by INFN
Magnet finished in 2010

## Slide 69
NICA-V accelerator complex
Nuclotron
45 Tm
E ~ 12 GeV
SC p-linac (10MV/m)
p-source
Two collider rings
SC magnets ~ 5 T;
~ 100 Tm
E ~ 30 GeV (p)
Intensity ~ 1e13
Booster (25 Tm)
Acceleration
up to
~ 1,3 GeV/u
Extracted high-intense p-beam
μ-target
Goal: MW proton beam to the target

## Slide 70
νe->νμ->ντ
Dubna
Baikal
~ 4500 km

## Slide 71
Nikola Camille Flammarion (1888)

## Slide 72
Спасибо за внимание !
My gratitude to: I.Meshkov, A.Sidorin, V.Kekelidze, A.Sorin, Yu.Oganessian et al for slides.

## Slide 73
B) Polarized Beams – Particle Spin Physics
The problem => Nucleon quark structure and nucleon spin
First hypothesis: 3 quarks are polarized in such a way that
Spin (p) = (u u d) =   1/2
However:
HERMES experiment at HERA eх p-collider
(DESY Lab., 1995 – 2007):
Not more 30% of proton spin can be explained with constituent
quarks, i.e. Nucleon spin   Squark
Modern hypothesis:
Snucleon = Squark + Sgluon + Lquark + Lgluon ,
L – orbital momentum of the quark/gluon
Introduction